## Slide 1
Aktorik und Sensorik mit intelligenten Materialsystemen 2
Computer Lecture 4: Comparison of Single-Crystal and Polycrystalline SMA models in Simulink
Gianluca Rizzello
gianluca.rizzello@imsl.uni-saarland.de Saarland University

## Slide 2: ASIM 2- Computer Lecture 4 overview
GOAL: simulate and compare the response of single-crystal and polycrystalline SMA dynamic models
Performance comparison at different loading/unloading rates
Partial unloading and minor loops
Simulation of SMA spring actuator

## Slide 3: Homework
Given the matlab scripts Parameter.m and Parameter_PC2.m, the Matlab s-functions sSMA_displacementIn.m and sSMA_displacementIn_PC2.m, and the Simulink files SMA_displacementIn.slx and SMA_displacementIn_PC2.slx
  Compare force vs. displacement and temperature vs. time responses for both single-crystal and polycrystalline models, and comment the main differences between results. For each simulation, set TE = 293 K and initial conditions x+(0) = 0, x-(0) = 0, T(0) = 293 K. Perform the following tests:
    Apply input displacement y(t) = 0.1 + 0.00085ft(1 + sin(2pft - p/2)) m, with different values of f = 0.01 Hz, 0.1 Hz. For each case, simulation time = 4/f s;
    Apply input displacement y(t) = 0.1 + 0.00225(1 + sin(2pft - p/2)) + 0.00075(1 + sin(10pft - p/2)) m, with different values of f = 0.01 Hz, 0.1 Hz. For each case, simulation time = 1/f s;
  Implement, for each model, a SMA spring actuator based on a linear spring with the following characteristics: k = 95.75 N/m, y0 = 0.125 m. Use TE = 293 K and the following initial conditions: single-crystal model, x+(0) = 1, x-(0) = 0, T(0) = 293 K; polycrystalline model, x+(0) = 0.96, x-(0) = 0, T(0) = 293 K. For each model, apply the following joule heating input J(t) = 0.2(1 + sin(2pft - p/2)) W, with different values of f = 0.1 Hz, 1 Hz, and plot the displacement vs. temperature and resistance vs. displacement responses for the first 2 cycles. Comment the differences between the results. HINT: for this simulation, to achieve more accurate results increase both tolerances of the polycrystalline model to 10-9.