## Slide 1
Aktorik und Sensorik mit intelligenten Materialsystemen 2
Computer Lecture 6: Dynamic Simulation of DEA with Different Biasing Elements
Gianluca Rizzello
gianluca.rizzello@imsl.uni-saarland.de Saarland University

## Slide 2: ASIM 2 - Computer Lecture 6 overview
GOAL: Simulate the response of DEA dynamic model when different biasing elements are used
Simulation of DEA biased with
  Mass
  Mass + linear spring (LBS)
  Mass + linear spring + nonlinear spring (NBS)
Actuator response for different driving signals

## Slide 3: Homework
  Given the matlab script Parameter.m, the matlab s-function sDE_dispIn.m, rhe matlab figure static_curves.fig, and the Simulink file DEA.slx:
  Consider three different DE actuators, each one combined with different biasing elements: 1.a) Mass: m = 0.5 Kg, g = 9.81 m/s2 1.b) Mass + LBS: m = 0.001 Kg, g = 9.81 m/s2, kl = 500 N/m, y0l = 0.08 m 1.c) Mass + LBS + NBS: m = 0.001 Kg, g = 9.81 m/s2, kl = 500 N/m, y0l = 0.0765 m, kn1 = 1000 N/m, kn7 = 5∙1013 N/m7, y0n = 0.065 m Create a Simulink block diagram for each actuator
  Simulate the displacement response of each of the three actuators to a square wave input voltage with duty cycle of 50%, ranging from 0 to 2500 V and having a period 10 s. Plot the time evolution of the displacement and comment the performance of the actuator in each of the three cases. HINT: use the plot static_curves.fig to generate the correct initial conditions for each simulation. Also remember that the initial viscoelastic strains must be equal to the initial material strain, which has to be specified in the Parameter.m file. Run several simulation cycles and plot the performance at periodic regime only.