## Slide 1
Aktorik und Sensorik mit intelligenten Materialsystemen 2
Computer Lecture 3: Dynamic Simulation of SMA Operating Against Loading Elements in Simulink
Gianluca Rizzello
gianluca.rizzello@imsl.uni-saarland.de Saarland University

## Slide 2: ASIM 2- Computer Lecture 3 overview
GOAL: Simulate the response of SMA dynamic model operating against different mechanical loads
Evaluation of heating/cooling dynamics on SMA response
Simulation of different SMA + load configurations:
  SMA vs mass
  SMA vs spring
  SMA vs spring + mass
Effects of variable environmental temperature

## Slide 3: Homework
Given the matlab script Parameter.m, the matlab s-function sSMA_displacementIn.m and the Simulink files SMA_displacementIn.slx, SMA_mass.slx
  Consider SMA_displacementIn.slx and the following inputs: J(t) = 0.2 W, TE = 293 K, y(t) = 0.1(1.035+0.035sin(2pft)) m, with f = 0.01,0.04, 0.1, 0.25, 1 Hz. Plot the resulting force-displacement curves, and comment them.
  Use SMA_mass.slx to simulate the response of a SMA-mass actuator, with m = 0.2 kg, g = 9.81 m/s2, TE = 293 K, and initial conditions x+(0) = 1, x-(0) = 0, T(0) = 293 K, y(0) = 0.1054 m, y’(0) = 0 m/s, to the following input Joule heating
  Plot the resulting force vs. time and displacement vs. time, and provide some comments. NOTE: all parameters are already preset, except for SMA initial conditions and input signal.
  Implement the Simulink block diagrams which allow to simulate the following loads:
    Spring, with k = 325.61 N/m, y0 = 0.1088 m, TE = 293 K, and initial conditions x+(0) = 1, x-(0) = 0, T(0) = 293 K
    Spring + mass, with k = 325.61 N/m, y0 = -0.4938 m, m = 20 kg, g = 9.81 m/s2, TE = 293 K, and initial conditions x+(0) = 1, x-(0) = 0, T(0) = 293 K, y(0) = 0.1049 m, y’(0) = 0 m/s
  For each case, simulate the response to the above Joule heating input, and provide comments.
  Consider the SMA – spring actuator of exercise 3.a. Repeat the simulation with TE = T(0) = 273 K. How does the displacement performance change? How do we need to modify the joule heating input to obtain the same displacement as in 3.a? Show simulation results and comment.