## Slide 1
Aktorik und Sensorik mit intelligenten Materialsystemen 2
Mid-Term Exam B:
Modeling and Simulaton of a Bundle of SMA Wires Driving an Hydraulic Valve
Stefan Seelecke
Gianluca Rizzello
stefan.seelecke@imsl.uni-saarland.de
gianluca.rizzello@imsl.uni-saarland.de Saarland University

## Slide 2: ASIM 2 Mid-Term Exam
We consider a bundle of N wires connected in parallel
All wires have same length y
Total force FTOT equals sum of forces
Total power JTOT is divided in N equal parts, and shared among wires
Total resistance RTOT is given by parallel of N resistances
NOTE: you can activate/deactivate SMA internal loops by setting params_PC2.internal_loops_flag = 1 or 0, respectively. Try to solve as much problems as possible with internal loops activated, and set the flag to 0 inly in case severe numerical problems occur
J
y
F
SMA Actuator
FTOT
N
JTOT
1/N
SMA Bundle
R
RTOT
1/N

## Slide 3: ASIM 2 Mid-Term Exam
The bunle of SMA wires is working against a mass-spring-damper load
Dynamic equation
Steady-state equation (time derivatives go to zero)
y
m
y0
k
b
…
…
SMA1
SMAi
SMAN
FTOT

## Slide 4: ASIM 2 Mid-Term Exam
We assume that TE = T0 = 293 K, and that the wires can stand a maximum increase of DT = 80 K from this initial value
Given a maximum increase of temperature of DT = 80 K, the maximum power JTOT which can be applied to the wire, denoted as JMAX, can be obtaind from the thermal equation, by setting all derivative equal to zero
JMAX has to be recalculated every time geometry/number of wires are modified
l0
r0

## Slide 5: ASIM 2 Mid-Term Exam
GOAL: design and simulate a bundle SMA actuator system which drives a hydraulic valve
Implement in Simulink the model of the SMA bundle. Simulate the SMA force/displacement hystesis loop of the SMA bundle y-FTOT for JTOT = 0 and JTOT = JMAX, for different wire lenghts l0 and number of SMA wires in the bundle N. When deforming the wire, design y in such a way the strain e ranges from 0 to 0.048, at 0.01 Hz. Show how hysteresys changes while changing both parameters. NOTE: If JMAX is chosen properly, the temperature of activated wire allways be equal 373 K (100 °C).
Assume the SMA bundle working against a linear spring with elastic constant k = 500 N/m only, at steady state. By using graphical method, design optimal values of SMA length l0, number of wires N, and spring pre-deflection y0 such that, when actuated with JMAX, the actuator produces a displacement (i.e., difference between off and on position) of at least 0.022 m.

## Slide 6: ASIM 2 Mid-Term Exam
By considering previously designed SMA and linear spring, simulate the response of a mass-spring-damper-SMA bundle actuator, described as follows Assume previously designed values for SMA length and number of wires, spring stiffness and pre-deflection, and use m = 0.3 kg, b = 10 N*s/m. Apply a square wave input joule heating from 0 to JMAX, with period 10 seconds and duty cycle of 50%, and plot temperature T over time and normalized stroke s over time, where where y is the current SMA length, and yin is the SMA length when the wire is not actuated (i.e., JTOT = 0). Both y and yin are expressed in meters. NOTE: do not forget to set reasonable initial conditions.

## Slide 7: ASIM 2 Mid-Term Exam
Assume that the SMA wire is used to drive a proportional hydraulic valve, whose flow rate q (unit: m3/s) is given as follows where r = 865 kg/m3 is the fluid density (oil), DP = 400000 Pa is the pressure difference of the valve, A = 0.0005 m2 is the cross-sectional area of the fully open valve,h = 0.9 is a loss factor, and

## Slide 8: ASIM 2 Mid-Term Exam
HINT: to implement sat(s), you can use saturation block in Simulink

## Slide 9: ASIM 2 Mid-Term Exam
Construct a block diagram for the overall SMA driven valve
By applying the square wave joule heating input from 0 to JMAX , period of 10 s, plot the resulting flow rate-resistance (q - RTOT) curve. Find the best line which approximates such a relationship in terms of coefficients a1 and a0, in the following form
y
SMA Bundle
JTOT
RTOT
LOAD
q
s
FTOT

## Slide 10: ASIM 2 Mid-Term Exam
Use previous relationship to reconstruct flow rate from resistance RTOT. Define as the flow rate estimated from resistance. Then, based on estimated flow rate , implement a sensorless PI flow rate control loop. Design the PI gains (e.g., via hand-tuning) in such a way the closed loop system is able to track constant step references sufficiently fast and without large overshoot/oscillations.
y
SMA Bundle
JTOT
RTOT
LOAD
q
s
FTOT

## Slide 11: ASIM 2 Mid-Term Exam
For the flow rate set-point q*, use Simulink to generate a uniform random number ranging from minimum to maximum attainable flow rate (corresponding to s = 0 and s = 1, respectively), with a period of 2 s.
Plot the resulting real flow rate, estimated flow rate, together with set point, and other relevant quantities (e.g., Joule heating).
q*
e
+
-
y
SMA Bundle
RTOT
LOAD
q
JTOT
PI
s
FTOT

## Slide 12: ASIM 2 Mid-Term Exam
In control loop, control input of SMA, i.e., JTOT, has to be limited between its physical limits 0 and JMAX with a saturation block.
In order to work properly with satuation, PI control has to be implemented in an anti-windup configuration. To do so, it is possible to use built-in blocks in Simulink.

## Slide 13: ASIM 2 Mid-Term Exam
    Results must be presented with a presentation done in PowerPoint (or any similar software), in either german or english, which includes plot of the most significant quantities and comments on the results.
    Results an be presented by groups of 3 people (or 2, if needed).
    For each group, 10 minutes presentation + 5 minutes for questions.
    MID-TERM EXAM B DATE: 15/06/2018, at 13:00